## Slide 1
SMART INDIA HACKATHON 2026
SMART INDIA
HACKATHON
2026
TITLE PAGE
•
Problem Statement ID – PS-04
•
Problem Statement Title – Space Debris Tracking & Satellite Collision Risk Prediction Dashboard
•
Theme – Space Technology
•
PS Category – Software
•
Team ID – << enter your Team ID >>
•
Team Name (Registered on portal) – << enter your Team Name >>
WORKING PROTOTYPE — MEASURED, NOT PROJECTED
859
real tracked objects screened
3,032
close approaches found in 72 h
62 / 62
known-answer engine tests pass
Runs entirely in the browser — no backend, no network at runtime.
A conjunction screening console that ranks close approaches AND states what would change the verdict.
Real element sets · real SGP4 · real times of closest approach. Every capability in the interface declares its own build status, so nothing unfinished can appear as working.
@SIH Idea submission- Template
Notes: PS-04. Fill in Team ID and Team Name before submitting — they are the only placeholders in this deck.

## Slide 2
Team
Name
KESSLER — Collision Risk Triage Console
SMART INDIA
HACKATHON 2026
@SIH Idea submission- Template
2
❖
Proposed Solution (Describe your Idea/Solution/Prototype)
HOW IT ADDRESSES THE PROBLEM
53,000+ alerts → 10 manoeuvres
ISRO, 2024. Detection is not the bottleneck — deciding which 10 of 53,000 matter is. KESSLER ranks and justifies that choice.
DETAILED EXPLANATION — WHAT THE PROTOTYPE DOES
1
INGEST
Public CelesTrak TLEs
859 real objects
▶
2
SCREEN
SGP4 + 3-stage cascade
368,511 pairs → 3,032
▶
3
RANK
Collision probability,
severity band, 0–100 score
▶
4
DECIDE
What would change
the verdict + CDM export
❖
Innovation and uniqueness of the solution
Answers "would this change your mind?"
Every event states the miss distance and the uncertainty multiplier that would drop it a severity band. Published tools give a ranked list and stop there.
An interface that cannot overstate itself
Every capability renders from one registry carrying its own status, so nothing unbuilt can appear as working. Our breakup model prints its own disagreement with the Fengyun-1C catalogue on every test run.
Speaks the operator’s format
Exports CCSDS 508.0-B-1 Conjunction Data Messages — what Space-Track, ESA and NASA CARA exchange — so output enters a real pipeline, not a spreadsheet.
Notes: Lead with the ratio. The innovation is epistemic, not algorithmic — say that out loud.

## Slide 3
Team
Name
TECHNICAL APPROACH
SMART INDIA
HACKATHON 2026
@SIH Idea submission- Template
3
❖
Technologies to be used
Frontend
React 18 · TypeScript · Vite · Tailwind
Orbital engine
SGP4 (satellite.js, AIAA 2006-6753)
Compute
Web Worker — off the main thread
Data
CelesTrak GP two-line element sets (free, no sign-up)
Interop
CCSDS 508.0-B-1 Conjunction Data Message · CSV
Deployment
Static files — one 1.7 MB self-contained HTML file
❖
Methodology and process for implementation
368,511
ALL PAIRS
859 objects, 72-hour horizon
100.000%
368,491
PERIGEE–APOGEE FILTER
Orbits that can never intersect
99.995%
253,010
COARSE SWEEP
60 s steps, 450 km gate
68.7%
3,032
CONFIRMED EVENTS
Refined to exact TCA by bisection
0.82%
121× reduction, and the first filter removes only 20 pairs — bar length ∝ log₁₀(count); every stage figure is measured by the run, not asserted
VERIFIED, NOT CLAIMED
3,710,880
SGP4 propagations per run (~15 s)
1.14×10⁻¹³ km
Cascade vs brute-force all-pairs agreement
≈1.73
Scaling exponent, 1.70–1.74 across runs (2.0 = all-pairs)
Notes: If asked about scale: measured with npm run scaling, six catalogue sizes, not extrapolated from theory.

## Slide 4
Team
Name
FEASIBILITY AND VIABILITY
SMART INDIA
HACKATHON 2026
@SIH Idea submission- Template
4
❖
Analysis of the feasibility of the idea
✓
Already built
Not a concept. A working console with a real screening engine, running today.
✓
Zero data cost
CelesTrak publishes TLEs free with no sign-up — the usual blocker for this theme.
✓
Zero infrastructure
No backend, no database, no server. Static hosting, or one offline file.
✓
Proven correct
62 known-answer tests, including brute-force cross-check of the whole cascade.
❖
Potential challenges and risks · Strategies for overcoming these challenges
RISK
WHY IT MATTERS
MITIGATION — ALREADY IN THE PROTOTYPE
TLEs carry no covariance
The 1σ uncertainty behind collision probability has to be assumed, and the ranking rests on it.
Disclosed at every point of use and exposed as a control you can sweep. Exported CDMs declare COVARIANCE_METHOD = DEFAULT. A measured path — successive TLE differencing — is implemented and recovers a known perturbation to 1.00×.
Screening a full 30,000-object catalogue
All-pairs cost grows quadratically; a naive screen would not finish.
Cascade measured at exponent ≈1.73 — 1.70–1.74 across runs, since it is fitted to elapsed times — so sub-quadratic. Next step is spatial binning per time step instead of a pair loop.
SGP4 drifts away from its epoch
Element sets are only trustworthy near the time they were fitted.
Element-set age is shown per object, feeds the uncertainty model, and the console clock is anchored to the snapshot instant rather than the wall clock.
Notes: The right-hand column is the slide to linger on — every mitigation is already built, not planned.

## Slide 5
Team
Name
IMPACT AND BENEFITS
SMART INDIA
HACKATHON 2026
@SIH Idea submission- Template
5
❖
Potential impact on the target audience
HIGH
CARTOSAT-2C × COSMOS 2251 DEB
An ISRO earth-observation satellite against a fragment of the 2009 Iridium 33 / Cosmos 2251 collision — found by our engine in a 72-hour screening run.
1.911 km
Miss distance
4.834 km/s
Closing speed
4.9×10⁻⁴
Collision probability
3.16 km
Would drop it a band
ISRO / IS4OM
A triage layer over the 53,000 alerts already arriving each year — and a second opinion that states its own uncertainty.
Universities & cubesat teams
The same pipeline as a large operator, with no licence, no analyst and no procurement. This is the access gap PS-04 names.
Indian NewSpace startups
20 of India’s 22 active LEO satellites face elevated collision risk. A first-launch operator can screen before and after deployment.
❖
Benefits of the solution (social, economic, environmental)
SOCIAL
Protects the satellites behind weather warning, disaster response, crop monitoring and navigation. A lost earth-observation satellite is a lost public service.
ECONOMIC
Commercial conjunction services are priced for large operators. Free public data plus an open engine removes both the licence and the analyst from the cost.
ENVIRONMENTAL
Debris outlives the collision: 813 fragments of the 2009 Iridium 33 / Cosmos 2251 crash are still in our snapshot 15 years on. Screening this one event models 19 new trackable fragments and an added collision rate on all 33 assets we assess.
STRATEGIC
Screening you can run yourself, on open data, is sovereign capability — supporting India’s Debris Free Space Missions target for 2030.
Notes: Every number on this slide is visible in the live demo. Do not round any of them.

## Slide 6
Team
Name
RESEARCH AND REFERENCES
SMART INDIA
HACKATHON 2026
@SIH Idea submission- Template
6
❖
Details / Links of the reference and research work
MODELS AND STANDARDS IMPLEMENTED IN THE PROTOTYPE
SGP4 propagation
Vallado & Crawford, "Revisiting Spacetrack Report #3", AIAA 2006-6753
Collision probability
Foster & Estes, NASA JSC-25898, 1992 — the model our Pc uses
Conjunction screening
Anilkumar et al., CLAPS — ISRO close-approach software, MCF Hassan
Debris generation
Johnson et al., NASA Standard Breakup Model, EVOLVE 4.0, 2001
Cascade risk
Kessler & Cour-Palais, J. Geophys. Res. 83(A6), 1978
Orbital decay & re-entry
King-Hele drag decay; Sutton–Graves stagnation-point heating
Message standard
CCSDS 508.0-B-1, Conjunction Data Message
Uncertainty from TLEs
Flohrer et al., TLE orbit error categorisation, AMOS 2008
DATA SOURCES AND INDIAN CONTEXT
CelesTrak GP catalogue
celestrak.org — free, no sign-up. 859 objects across 5 groups.
ISSAR 2024
isro.gov.in/ISSAR_2024.html — 53,000+ alerts, 10 CAMs in 2024
Lok Sabha reply, Aug 2026
20 of 22 active Indian LEO satellites at elevated risk; 20 CAMs flown in 2025
Debris Free Space Missions
isro.gov.in/Debris_Free_Space_Missions.html — India’s 2030 target
WHY THERE IS NO MACHINE-LEARNING MODEL
ESA ran this exact competition on 13,154 real conjunction events. The naive baseline — reuse the risk in the most recent CDM — beat almost every model submitted; a later benchmark found roughly 1 model in 5,000 beat it, by 1.4%. We spent that effort on measuring uncertainty instead.
PROTOTYPE, ENGINE AND EVERY FIGURE IN THIS DECK
github.com/agpriyanshu07/SIH-Internal-NITR-2
npm run validate reproduces all 62 engine checks · npm run screen reproduces all 3,032 events · npm run scaling re-measures the ≈1.73 scaling exponent
No figure in this presentation is estimated, projected or illustrative. Each one is either measured by the prototype or cited above.
Notes: Expect the AI question. This slide answers it with numbers rather than defensively.