## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – PS-04
Problem Statement Title – Space Debris Tracking & Satellite Collision Risk Prediction Dashboard
Theme – Space Technology
PS Category – Software
Team ID – <TEAM ID>
Team Name (Registered on portal) – <TEAM NAME>
THE IDEA
KESSLER
A conjunction screening console that ranks which close approaches are worth acting on — and says what would have to be true for each one to stop mattering.
859 OBJECTS · 3,032 EVENTS / 72 h · NO BACKEND

## Slide 2: KESSLER Conjunction screening console for Low Earth Orbit
<TEAM NAME>
PROPOSED SOLUTION · DESCRIBE YOUR IDEA / SOLUTION / PROTOTYPE
An operations console for Low Earth Orbit: it finds every close approach in the catalogue, ranks them, and defends the ranking.
15.1 s
FULL RUN
3,032
EVENTS / 72 H
859
OBJECTS
DETAILED EXPLANATION OF THE PROPOSED SOLUTION
Screen, rank, explain
▪ Public CelesTrak TLEs → SGP4 propagation → exact time of closest approach → a 0–100 risk score.
▪ A cascade takes 368,511 pairs to 3,032 events in 15 s — in the browser.
▪ Every figure is measured; the one assumed input, σ, is shown where it is used.
HOW IT ADDRESSES THE PROBLEM
Triage, not detection
▪ Nobody needs help finding conjunctions — 53,000 arrive unbidden. Judgement is scarce.
▪ Each event carries a triage verdict: what would have to change for it to stop mattering.
▪ CARTOSAT-2C would need to miss by 3.16 km, not 1.911 — that one is measurable.
INNOVATION AND UNIQUENESS OF THE SOLUTION
An interface that cannot overstate itself
▪ One registry declares every capability live / partial / not built — the UI renders from it.
▪ It continues past the conjunction: breakup, decay, re-entry survival, cascade rate.
▪ Exports CCSDS CDMs — output enters an operator’s existing pipeline.
2D ORBITAL VIEWER · FLAGGED-CONJUNCTION LAYER · REAL ELEMENT SETS

## Slide 3: TECHNICAL APPROACH
<TEAM NAME>
TECHNOLOGIES TO BE USED · METHODOLOGY AND PROCESS FOR IMPLEMENTATION
Four stages, each one derived rather than tuned — the same cascade ISRO’s CLAPS uses, reached from the physics and then found to match.
62/62
CHECKS PASS
3.7 M
SGP4 CALLS / RUN
~400
LINES OF ENGINE
WORKING PROTOTYPE

## Slide 4: FEASIBILITY AND VIABILITY
<TEAM NAME>
ANALYSIS OF FEASIBILITY · POTENTIAL CHALLENGES AND RISKS · STRATEGIES TO OVERCOME
It is already built and already measured — the full pipeline runs offline, on free data, from a fresh clone.
0
NETWORK CALLS
₹0
DATA LICENCE
WHY WE KNOW IT WORKS · NPM RUN VALIDATE
62 of 62 known-answer checks pass from a fresh clone
▪ Cascade vs brute force — 505 candidates both ways, 0 missed, 0 extra; minimum distances agree to 1.14 × 10⁻¹³ km.
▪ Breakup model vs three real events — Cosmos 1408 0.80×, Iridium/Cosmos 0.53×, Fengyun-1C 0.33×. The disagreement prints on every test run rather than being tuned away.
▪ Burn advisor — re-propagated displacement agrees with the closed form to 3.9%.
▪ Deterministic — re-running the screen reproduces all 3,032 events byte for byte.
RISK 01 · DATA
TLEs are not precision ephemerides
SGP4 along-track error is kilometre-scale and grows with element-set age — the same size as the miss distances reported.
MITIGATION
σ = 0.9 km + 0.055·age feeds every score, and a max-age threshold withholds stale predictions rather than showing them.
RISK 02 · MODEL
A TLE carries no covariance
Pc rests on an assumed σ — the weakest link in the ranking, and the easiest one to hide.
MITIGATION
Every CDM declares COVARIANCE_METHOD = DEFAULT; σ is a live control that re-bands the whole board on screen.
RISK 03 · SCALE
The real catalogue is 30,000 objects
All-pairs is O(n²): 30,000 objects is roughly 450 million pairs, not 368,511.
MITIGATION
Measured, not asserted — exponent 1.738 over six catalogue sizes. Next step is spatial binning per time step.
RISK 04 · INPUTS
Masses and cross-sections are assumed
Fragment count scales as mass⁰·⁷⁵, and a TLE carries neither mass nor geometry.
MITIGATION
Every such assumption is a slider, not a constant — sweep it and watch the answer move.

## Slide 5: IMPACT AND BENEFITS
<TEAM NAME>
POTENTIAL IMPACT ON THE TARGET AUDIENCE · BENEFITS OF THE SOLUTION
The operators who most need conjunction screening are exactly the ones who cannot buy it.
₹0
LICENCE + DATA
5,300 : 1
ALERTS PER DECISION
SPACE AGENCIES & NATIONAL OPERATORS
A triage layer over public data that says which pair to escalate for a real CDM. 72 of the 3,032 events in the demo run involve an ISRO-operated asset.
UNIVERSITIES, CUBESAT TEAMS, STARTUPS
The entry cost of commercial CA is the licence plus the analyst. This needs neither — one cubesat gets the same pipeline as four hundred satellites.
STRATEGIC AUTONOMY
Asking a foreign vendor “is my satellite about to be hit” is a dependency that is not commercially negotiable in a crisis.
SOCIAL
Not a procurement decision
▪ Open engine, open data, every assumption stated where it is used.
▪ No licence to negotiate, and nothing you are contractually barred from inspecting.
ECONOMIC
Zero licence, zero data cost
▪ Commercial CA is priced for constellation operators — the entry cost is the licence plus the analyst.
▪ One avoided collision protects an asset worth hundreds of crores.
ENVIRONMENTAL
Orbit is a shared resource
▪ Low Earth Orbit has no traffic control, and 20 of India’s 22 active LEO satellites already face elevated risk.
▪ Ranking which passes matter is how the Kessler cascade stays hypothetical.
OPERATIONAL
Fits the pipeline that exists
▪ CCSDS CDM export drops straight into an operator’s flight-dynamics workflow.
▪ Runs offline from a single file — a demo that never depends on the venue’s wifi.

## Slide 6: RESEARCH AND REFERENCES
<TEAM NAME>
DETAILS / LINKS OF THE REFERENCE AND RESEARCH WORK
Every model here is a published one applied to real data, and every claim the console makes has a test behind it.
62
TESTS PASSING
10
MODELS & STANDARDS
MODELS AND STANDARDS IMPLEMENTED — NOT CITED, IMPLEMENTED
01 Vallado & Crawford — Revisiting Spacetrack Report #3 (SGP4) AIAA 2006-6753
02 Foster & Estes — Parametric analysis of orbital debris collision probability NASA JSC-25898, 1992
03 Johnson et al. — NASA’s New Breakup Model of EVOLVE 4.0 Adv. Space Res. 28(9), 2001
04 Kessler & Cour-Palais — Collision frequency of artificial satellites JGR 83(A6), 1978
05 King-Hele — Satellite Orbits in an Atmosphere: Theory and Applications 1987
06 Sutton & Graves — General stagnation-point convective-heating equation NASA TR R-376, 1971
07 Allen & Eggers — Motion and aerodynamic heating of ballistic entry NACA TR-1381, 1958
08 CCSDS 508.0-B-1 — Conjunction Data Message Blue Book, 2013
09 Flohrer et al. — Categorisation of TLE orbit errors for the SSN catalogue AMOS 2008
10 Anilkumar et al. — CLAPS, ISRO close-approach prediction software MCF Hassan / IS4OM
Each of these is implemented in src/data/engine/, not merely cited — and every one is exercised by the validation suite.
DATA SOURCES AND PRIOR ART
▪ CelesTrak GP element sets — celestrak.org. Free, no signup, five groups, 859 objects, captured 2024-11-17T23:05Z.
▪ ISRO Indian Space Situational Assessment Report — IS4OM. Source of the 53,000 alerts and 10 manoeuvres.
▪ CelesTrak SOCRATES — the closest public prior art. Upstream truth we would happily consume; what we add is interrogability and the consequence chain.
▪ ESA Spacecraft Collision Avoidance Challenge — 13,154 real CDMs, 97 teams. The evidence behind the panel below.
▪ 18th / 19th Space Defense Squadron — issuer of the operational CDMs with a real covariance. This tool tells a small operator which pair to go and ask about.
WHY THERE IS NO MACHINE-LEARNING MODEL
ESA ran exactly this experiment: 13,154 real conjunction events as CDMs, 97 registered teams. The naive baseline — predict the risk stated in the most recent CDM — beat almost every model submitted, and a later systematic benchmark found roughly one model in five thousand beat it on both training and test sets, by 1.4%.
So a model here would be decoration we could not validate, inside a project whose entire argument is that every claim has a test behind it. We spent that effort on successive TLE differencing instead — the published method for measuring positional uncertainty from public element sets alone, tested against a known injected perturbation, which it recovers to 1.00×.
REPRODUCE EVERY NUMBER IN THIS DECK
github.com/agpriyanshu07/SIH-Internal-NITR-2
npm run validate → 62/62 known-answer checks
npm run screen → reproduces all 3,032 events
npm run scaling → the measured 1.738 curve
npm run build:single → one offline HTML file