## Slide 1
PS-04
KESSLER
Space debris tracking and satellite collision risk prediction
A conjunction screening console that ranks which of fifty thousand close approaches is worth acting on — and says what would have to be true for each one to stop mattering.
859 objects
REAL CELESTRAK TLES
3,032 events
FROM 368,511 PAIRS
62/62
KNOWN-ANSWER TESTS
0 kB
BACKEND, AND NETWORK AT RUNTIME
Software · Space Technology · Internal Hackathon 2026
Notes: Open on the ratio, not on the technology. 53,000 alerts, 10 manoeuvres. Everything on this slide is reproducible by a command in the repository.

## Slide 2
THE PROBLEM
Detection is solved. Triage is not.
ISRO generated more than 53,000 close-approach alerts for Indian satellites in 2024 and flew ten collision avoidance manoeuvres. Nobody needs software that finds close approaches — they arrive unbidden. What is scarce is the judgement to discard the other 52,990.
And the tools that do this are expensive, closed, or priced for operators with a flight-dynamics team. A university group flying one cubesat has the problem and none of the access.
INDIA, 2024–26
53,000+
CLOSE-APPROACH ALERTS GENERATED
Indian Space Situational Assessment Report 2024
10
MANOEUVRES FLOWN
5,300:1
SCREENED PER DECISION
20 of 22
ACTIVE INDIAN LEO SATELLITES AT ELEVATED RISK
Sources: ISSAR 2024 (ISRO/IS4OM); Lok Sabha reply, August 2026.
Notes: This ratio is the problem statement, whatever the official wording says. Say the two numbers slowly.

## Slide 3
PROPOSED SOLUTION
Would this change your mind?
1
Screen
SGP4 over public TLEs. A three-stage cascade takes 368,511 pairs to 3,032 confirmed events, each with an exact time of closest approach found by bisection — not by sampling.
2
Rank
Foster-style collision probability, severity bands, and a 0-100 score whose weights and per-term contributions are printed on the event, so the ranking can be defended rather than only reproduced.
3
Decide
The counterfactual, per event: the miss distance that would drop it a band, the uncertainty multiplier that would do the same, and whether the verdict is geometry or an artefact of an assumption.
4
Hand off
CCSDS 508.0-B-1 Conjunction Data Messages — the format Space-Track, ESA and NASA CARA exchange — so the output enters a pipeline instead of ending in a spreadsheet.
Innovation: the interface renders every capability from one registry that carries its own status, so it is structurally incapable of presenting something unbuilt as working.
Notes: Point at row 3. That is the differentiator — published tools stop at row 2.

## Slide 4
TECHNICAL APPROACH
The same cascade ISRO published for CLAPS
We built this from the physics, then found ISRO's published description of the tool it runs at MCF Hassan. The architectures match stage for stage — convergence, not reimplementation.
368,511
All pairs
859 objects, 72-hour horizon
▸
368,491
Perigee–apogee
Orbits that can never meet
▸
253,010
Velocity-bounded
60 s sweep, 450 km gate
▸
3,032
Refined to true TCA
Bisection on range rate
The 450 km gate is derived, not tuned
15 km/s maximum closing speed × 60 s step ÷ 2. Shrinking it makes the screen look faster while silently missing real approaches. CLAPS derives its own sieve the same way, from twice escape velocity — the same physical bound.
React · TypeScript · satellite.js · Web Worker
3,710,880 SGP4 propagations in ~15 s. The build-time precompute and the in-browser re-run are the same module, so they cannot disagree. Measured scaling exponent 1.738 against 2.000 for pure all-pairs.
Notes: If asked about scale: we measured it rather than arguing it. npm run scaling.

## Slide 5
FEASIBILITY AND VIABILITY
Built, tested, and honest about its limits
WHAT IS MEASURED
Objects, element sets, epochs, SGP4 propagation, times of closest approach, miss distances and relative velocities
Every figure in the pair-reduction cascade
The burn advisor’s re-propagated post-burn miss distance
62 known-answer tests, including brute-force all-pairs agreement to 1.14 × 10⁻¹³ km
The breakup model checked against three real catalogued events — and its Fengyun-1C disagreement printed on every run
WHAT IS ASSUMED, AND DISCLOSED WHEREVER USED
The 1σ positional covariance feeding Pc — a TLE carries none
Radar cross-section class, inferred from object type
Object masses for the consequence chain, where fragment count scales as mass^0.75
Every one of these is a control you can sweep, not a constant — and every exported CDM declares COVARIANCE_METHOD = DEFAULT so the assumption survives leaving the app
Risk we chose to carry: the demo screens a committed snapshot, not a live feed, because every element set must share one epoch for the run to mean anything. One command re-pulls from CelesTrak.
Notes: The right-hand column is the slide to linger on. Volunteering the limits is the point.

## Slide 6
IMPACT AND BENEFITS
One real event, taken all the way through
CJ-34550-41599 · HIGH · RISK SCORE 80
CARTOSAT-2C × COSMOS 2251 DEB
An ISRO earth-observation satellite against a fragment of the 2009 Iridium 33 / Cosmos 2251 collision, fifteen years later.
1.911 km
MISS DISTANCE
4.9×10⁻⁴
COLLISION PROBABILITY
72
ISRO-involved events, of the 2,901 that pass the default thresholds
3.16 km
The miss distance at which this event would drop a band — 1.25 km more than SGP4 found
0.47×
The uncertainty multiplier that would do the same. A large revision, so this band is geometry, not assumption
Who this reaches
It runs from a single file with the wifi off, on free no-signup data, with no licence and no analyst. A university group with one cubesat gets the same pipeline as an operator with four hundred satellites — which is the access gap the problem statement names.
Notes: Every number here is on screen in the live demo. Do not round any of them.

## Slide 7
RESEARCH AND REFERENCES
What we read — and what we chose not to build
MODELS AND STANDARDS IMPLEMENTED
Vallado & Crawford, SGP4 — AIAA 2006-6753
Foster & Estes, collision probability — NASA JSC-25898, 1992
Johnson et al., NASA Standard Breakup Model — EVOLVE 4.0, 2001
King-Hele, satellite orbital decay; Sutton–Graves stagnation-point heating
Kessler & Cour-Palais, particle-in-a-box cascade rate — JGR, 1978
CCSDS 508.0-B-1, Conjunction Data Message
Flohrer et al., TLE orbit error categorisation — AMOS 2008
Anilkumar et al., CLAPS — ISRO close-approach prediction software
WHY THERE IS NO ML MODEL
ESA ran this exact competition on 13,154 real conjunction events. The naive baseline — predict the risk in the most recent CDM — beat almost every model submitted. A later benchmark found one model in roughly five thousand beat it, by 1.4%.
So a model here would be decoration we could not validate, inside a project whose argument is that every claim is backed by a test.
We spent that effort on measuring σ instead.
Prototype, engine and every figure in this deck: github.com/agpriyanshu07/SIH-Internal-NITR-2 · npm run validate reproduces all 62 checks
Notes: Expect the AI question. This slide is the answer, and it scores rather than defends.